## Slide 1
LibriSense
An adaptive smart library
Dennis Gunt · Haoyang Chen · Niclas | Smart Cities and the IoT · University of Stuttgart | 20 July 2026
Notes: One line: our library notices you, thinks ahead and acts on its own. Everything runs live on this desk: two Raspberry Pis, real sensors, a real lamp.

## Slide 2
WHY
A hot summer, a full library
35 °C+
record heat sends students into the cool, quiet library
~40 %
of EU energy consumption happens in buildings
24/7
lighting and ventilation usually run on fixed schedules, not on demand
Our project: a reading zone that controls light, air quality and break timing automatically, with transparent decisions.
Notes: Opening story: this summer is brutal, libraries are packed. Light, air and breaks are constant trade-offs that nobody actively manages. That is a planning problem, so we gave the room a planner.

## Slide 3
SYSTEM OVERVIEW
Sensors, actuators and functionality
Sensors · 5
Actuators · 6
Functionality
Motion / occupancy · 2 Hz
physical
Illuminance · 2 Hz
physical
CO₂ concentration proxy
simulated
Outdoor weather (REST API)
software
Focus-session FSM (4 states)
software
Reading lamp · ZigBee relay
physical
Break LED
physical
Break buzzer · PWM, quiet
physical
Status LCD · CO₂ traffic light
physical
Window ventilation · 2 levels
virtual
Dashboard break banner
software
Light the seat when occupied and dark; off when empty
Air the room by pulse or full opening, picked by cost
Suggest breaks via LED + buzzer after 2 min of focus
Show state + current plan on dashboard and LCD
Re-plan on every state change; recover in < 1 s
2 physical sensors + 4 physical actuators on the desk · simulated parts are always labelled as such
Notes: Green tags are real hardware you can touch on the desk. Blue means simulated or virtual, always labelled honestly: our kit has no CO2 sensor and no motorised windows, so both are modelled and react realistically to planner actions.

## Slide 4
ARCHITECTURE
Eight modules, communicating only via MQTT
Sensing
motion · light · weather
→
Context
world state · CO₂ · FSM
→
Problem Gen.
state → PDDL + costs
→
Planner
Fast Downward
→
Execution
dispatch actions
MQTT bus (Eclipse Mosquitto) · retained topics: sensors → state → problem → plan → actions → actuator feedback
2 machines
Pi 5 runs broker, context, planner, dashboard (7 services). Pi 3 B+ runs sensors, actuators, LCD (3 services).
Closed loop
Actuator effects are sensed again and trigger re-planning. No module calls another directly.
Self-contained demo
The core Pi spans its own WiFi access point; edge Pi and dashboard laptop join it.
Notes: Covers modularity, indirect communication and distribution in one picture. Every arrow is a retained MQTT topic, so any module can restart and resynchronise instantly.

## Slide 5
AI PLANNING · 1/2
The model: classical PDDL with action costs
(:action pulse_ventilate_step
:parameters (?z - zone)
:precondition (and (occupied ?z)
(co2_high ?z))
:effect (and (not (co2_high ?z))
(co2_elevated ?z)
(increase (total-cost)
(pulse-vent-cost))))
(:goal (and (not (dark r1))
(not (co2_high r1))
(not (co2_elevated r1))))
(:metric minimize (total-cost))
real excerpt from librisense.pddl
1 type · 8 predicates
zone; occupied, dark, lamp_on, co2_elevated, co2_high, ventilating, break_due, break_suggested
6 actions, all cost-annotated
lamp on/off · suggest_break · pulse / pulse-step / full ventilation
Discretisation thresholds
dark below 40 % light · CO₂ bands at 800 and 1100 ppm · FSM sets break_due
Costs are per-instance fluents
pulse = 3 fixed · full = 4 + ΔT/2 with ΔT = max(0, 22 °C − T_outdoor), from the heat-loss relation Q ∝ Q_v · ΔT
Continuous values are discretised before planning, so the domain stays classical and plans remain provably optimal.
Notes: The action shown is the interesting one: a short pulse knocks high CO2 down one band only. Together with full_ventilate this gives the planner two genuinely different strategies for the same goal. Costs are static fluents written into each problem instance by the generator, computed from live outdoor temperature.

## Slide 6
AI PLANNING · 2/2
Solving: A* + LM-Cut, optimal in ~130 ms
library/state
→
discretise + goals + costs
→
PDDL instance
→
Fast Downward astar(lmcut())
→
library/plan
Generated whenever the discretised state or the costs change, plus a 30 s heartbeat. Only achievable goals are emitted, so every instance is solvable; an empty goal set skips the planner entirely.
Same state (occupied, CO₂ high), different weather:
5 °C outside
pulse 3 · full 12
[pulse_ventilate_step, pulse_ventilate]
total cost 6, beats 12 · winter airing: two short pulses, heat stays inside
29 °C outside
pulse 3 · full 4
[full_ventilate]
total cost 4, beats 6 · summer airing: one long opening clears the air fastest
LM-Cut is admissible, so A* returns minimal-cost plans. The winter strategy is not hard-coded; it results from the weather-dependent action costs.
Notes: Technical Q&A ammunition: search is A* with the LM-Cut admissible heuristic, so plans are cost-optimal, not just satisficing. Whole planner invocation including translation is about 130 ms on the Pi 5; pure search under 2 ms at this problem size. Unsolvable and timeout cases are handled explicitly, and the generator never emits a goal without an achieving action.

## Slide 7
LIVE
Live demo procedure
1
Sit down
occupancy detected, focus session starts
2
Cover the light sensor
zone turns dark, the real lamp switches on
3
Switch the lamp off manually
the disturbance is detected and corrected in under 1 s
4
Keep focusing
after 2 min: LED and gentle buzzer suggest a break
5
CO₂ rises
the planner opens the windows on the floor plan, CO₂ falls again
6
Walk away
zone empties, lamp switches off to save energy
We start on the simulated 6-seat floor plan for context, then hide it and focus on the one real seat.
Notes: Role split: person A at the desk triggers each moment, person B narrates the dashboard, person C explains the plan card whenever it changes. Keep this slide up during the live part as the run-sheet.

## Slide 8
COURSE REQUIREMENTS
All six requirements are met
✓
System distribution
2 Raspberry Pis, own WiFi in demo mode, 10 systemd services
✓
Indirect communication
MQTT publish/subscribe only, retained latest-value topics
✓
AI planning
PDDL domain, auto-generated instances, Fast Downward, cost-optimal
✓
IoT
5 sensors (2 physical) · 6 actuators (4 physical)
✓
System design
8 decoupled modules, each independently restartable
✓
Visualisation
current state + latest plan on dashboard and on-site LCD
plans in ~130 ms · closed-loop correction < 1 s · state at 2 Hz
Notes: Do not read the table aloud; point at the measured numbers at the bottom. These are from the running system, not estimates.

## Slide 9
LESSONS LEARNED
Sound sensor removed
it could not measure loudness over the slow GrovePi bus, so we removed it instead of publishing noise as data.
Unsolvable goals prevented
an early bug asked the planner to brighten a zone whose lamp was already on. The generator now emits only achievable goals.
CO₂ and windows are simulated
both are modelled, clearly labelled, and react realistically to planner actions.
WiFi reliability
client isolation, band steering and power-save caused repeated dropouts, so the demo runs on its own access point.
Questions?
Code, PDDL domain, docs and this deck: github.com/Dennis1911/librisense-smart-library
Notes: Q&A prep. Why planning, not rules? For one seat rules would do; the value is declared goals, per-instance costs and provable optimality, and it scales by adding actions instead of case distinctions. Why classical, not HTN? No task hierarchy needed; a discretised world fits classical planning with action costs exactly. What is real? Motion, light, lamp, LED, buzzer, LCD, weather. CO2 and windows are simulated and labelled.